## Slide 1: Bioeconomy evaluation methods and tools in the agro-farming sector
Antra Kalnbaļķīte, RTU, Latvia
Ilze Vamža, RTU, Latvia
MODULE 2
Bioeconomy, agrobiodiversity, biomass use, strategies and resources for sustainable rural development
UNIT 3
Bioeconomy evaluation methods in the agro-farming sector
Notes: Welcome to today lecture. I am Prof. Francesco Romagnoli from the Institute of Energy Systems and Environment at the Riga Technical University. I am happy to share with you the contents of the lecture on “Real case studies about Life Cycle Thinking -based methods and quantitative tools.

## Slide 2: Aim/objectives
Learners will be aware of the general bioeconomy assessment methods and tools with an emphasis on MCDA methods and tools (Value of bioresources based on indicator-based approach), Nexus approach, indicator analysis, and Cascade analysis of biorefinery within the agro-farming sector.

## Slide 3: Learning outcomes
LOut 12. Acquire a basic knowledge on the potential definition of strategic sustainable development of the agro-farming sector
LOut 16. Analyse different scenarios of bioeconomy implementation for specific situations, find the most optimal solution and make recommendations
LOut 18. Compare and analyse solutions from the application of LCA-based quantitative assessment and their implication on selecting a specific bioeconomy solution
LOut 20. Explain the different effects on the application of specific bioeconomy strategies within the agro-farming sector
LOut 23. Justify and recommend potential improvements solutions following a bioeconomy evaluation approach

## Slide 4: Keywords
Life Cycle thinking
Sustainability
Bioeconomy strategy solutions
Economic assessment
Social Assessment
Comparative assessment
LCA tools
Multi Criteria Analysis (MCA)
Nexus approach
Cascade approach

## Slide 5: Table of contents
Multi Criteria Decision Analysis (MCDA)
Nexus and Cascade approaches
Notes: This lecture is organized into 4 main parts: example of application and case studies on MCA, Nexus and Cascade approached. The last part puts an emphasis on a case study of the Life Cycle Sustainability Assessment for biofuel.

## Slide 6: Multi Criteria Decision Analysis
Antra Kalnbalkite, RTU, Latvia

## Slide 7: Decision making
Multicriteria Decision Analysis (MCDA) or Multicriteria Decision Making (MCDMaking) is a discipline that aims to support decision makers facing multiple and conflicting assessments.
The MCDA aims to highlight these conflicts and reach a compromise solution in a transparent process.
MCDA methods are designed to improve the quality of decisions by incorporating multiple criteria, making choices clearer, more rational and more effective.
The aim is to create a structured process to set goals, create alternatives and compare them from different perspectives.
The applications of MCDA are diverse and can cover environmental planning, fisheries management, water management, forestry, nuclear accident management, climate policy, life cycle analysis, etc.

## Slide 8: Types of decisions:
Roy (1981) has identified 4 main types of decisions:
Choice problem - the goal is to select the single best option or reduce the group of options to a subset of equivalent or incomparable ‘good’ options.
Sorting Problem – Options are sorted into ordered and predefined groups, called categories. The aim is to then regroup the options with similar behaviors or characteristics for descriptive, organizational or predictive reasons.
Ranking the problem options are ordered from best to worst by means of scores or pairwise comparisons
Describing Problem - The goal is to describe options and their consequences. This is usually done in first step to understand the characteristics of the decision problem.

## Slide 9: The most popular methods
Choice problems | Ranking problems | Sorting Problems | Describtion problems
AHP | AHP | AHP SORT | 
ANP | ANP |  | 
MAUT/UTA | MAUT/UTA | UTADIS | 
MACBETH | MACBETH |  | 
PROMETHEE | PROMETHEE | FLOWSORT | GAIA, FS - GAIA
ELECTRE | ELECTRE II, III, IV | ELECTRE-Tri | 
TOPSIS | TOPSIS |  | 
GOAL PROGRAMMING |  |  | 
DEA | DEA | Avots: Ishizaka A., Nemery P. Multi-Criteria Decision Analysis. Methods and Software. Wiley & Sons Ltd.: 2013, p. 299, ISBN: 978-1-119-97407-9 | 
AHP – Analytic hierarchy process, ANP – Analytic network process, MAUT – Multi-attribute utility theory, MACBETH – Measuring Attractiveness by Categorical Based Evaluation Technigue, PROMETHEE – Preference Ranking Organization METHod for Enriched Evaluation, ELECTRE – Elimination and choice expressing the reality, TOPSIS – Technique of Order Preferance Similarity to the Ideal Solution, DEA – Data Envelopment Analysis

## Slide 10
Problem | MCDA methods | Software
Ranking, description, choice Ranking, choice | PROMETHEE-GAIA | Decision Lab, D-Sight, Smart Picker Pro, Visual Promethee
 | PROMETHEE | DECERNS
 | ELECTRE | Electre IS, Electre III-IV
 | UTA | Right Choice, UTA+, DECERNS
 | AHP | MakeItRational, ExpertChoice, Decision Lens, HIPRE 3+, RightChoiceDSS, Criterium, EasyMind, Questfox, ChoiceResults, 123AHP, DECERNS
 | ANP | Super Decisions, Decision Lens
 | MACBETH | M-MACBETH
 | TOPSIS | DECERNS
 | DEA | Win4DEAP, Efficiency Measurement System, DEA Solver Online, DEAFrontier, DEA-Solver PRO, Frontier Analyst
Choice | Goal programming | -
Sorting, Description | FlowSort – FS - GAIA | Smart Picker Pro
Sorting | ELECTRE - Tri UTADIS AHPSort | Electre Tri, IRIS - - 17

## Slide 11: Required inputs for MCDA sorting methods
 | Inputs | Effort input | MCDA method | output
Sorting method | utility function | High | UTADIS | Classification by scoring
 | Pairwise comparison on ratio scale |  | AHPSort | Classification by scoring
 | Indifference, preference and veto thresholds |  | ELECTRE-TRI | Classification with pairwise outranking degrees
 | Indifference and preference thresholds | Low | FLOWSORT | Classification with pairwise outranking degrees and scores

## Slide 12: Required input for MCDA rank and choice methods
 | Inputs | Effort input | MCDA method | Output
Ranking/choice problem | Utility function | Very high | MAUT | Complete ranking with scores
 | Pairwise comparisons on a ratio scale and Interdependence |  | ANP | Complete ranking with scores
 | Pairwise Comparison on an interval scale |  | MACBETH | Complete ranking with scores
 | Pairwise comparison on a ratio scale |  | AHP | Complete ranking with scores
 | Indifference, preference and veto thresholds |  | ELECTRE | Partial and complete rating
 | Indifference and preference thresholds |  | PROMETHEE | Partial and complete rating
 | The ideal option and constraints |  | Goal programming | Feasable solution with deviation score
 | The ideal and anti-ideal solution |  | TOPSIS | Complete rating with proximity to ideal rating
 | No subjective input required | Very low | DEA | Partial rating with efectiveness score

## Slide 13: Establishment of criteria
Basic principles to be followed when defining the most important criteria:
Systematic principle- Criteria should reflect the main characteristics and functioning of the problem. Evaluating inclusive criteria provides much better results than evaluating one criterion
Principle of consistency - logical justification of choice of criteria
Independence principle - different criteria have to be chosen which are not directly or indirectly repeated
Principle of measurability - criteria must be measurable
Comparability principle - the criteria are comparable
* Alternative options - options from which to choose the best, the most appropriate
* Criteria - affects the choice of alternative

## Slide 14: Representation of decision levels /example/

## Slide 15: TOPSIS (Technique of Order Preference Similarity to the Ideal Solution)
For the environmental strategy and sustainable production and engineering, the TOPSIS method was used in 40% of cases
Advantages of TOPSIS:
  unlimited criteria and range of performance attributes,
  the choice of alternatives to understand the difference and the similarity of the alternative, to avoid double comparison (as in AHP),
  relatively simple calculation process,
  no special program is required
Disadvantage: No correlation between attributes
A1, A2, A3 … An – alternatives
x1, x2, x3… xm – criteria by which alternatives are evaluated
TOPSIS matrix

## Slide 16: TOPSIS method
The ideal alternative - the best option
(maximum benefit with minimal cost)
Contrary the (anti) ideal alternative - worst case scenario (minimal benefits, maximum costs)
TOPSIS compares alternatives by defining criteria / indicators for alternatives, determining the weight of each criterion/indicator, normalizing results and calculating the distance between each alternative
It is possible to compare alternatives that would otherwise not be comparable
The key concept is that the alternative you choose should be as close as possible to the ideal solution.
The ratio between the distance from the negative ideal and the sum of the distance from the ideal to the negative alternative is calculated.
Criteria 2
Anti-ideal solution
Ideal solution
Criteria 1

## Slide 17: AHP method
Pairwise comparison
(possibility to compare criteria by determining their significance)
The results are calculated
Consistency check have to be performed, to detect possible contradictions in the entries
C | i1 | i2 | i3 | i4
i1 | 1 | 5 | 7 | 9
i2 | 1/5 | 1 | 4 | 6
i3 | 1/7 | 1/4 | 1 | 4
i4 | 1/9 | 1/6 | 1/4 | 1
Consistency ratio, CR
RI – Random Index*
If CR > 0.1, ratings are inconsistent and need to be revised
*Random consistency index (RI) – dots lielums Saaty scale
Number of comparisons= 4 (4-1)/2=6
6
Consistency must be evaluated
Number of criteria=n
Number of comparisons= n (n-1)/2

## Slide 18: Weight determination (AHP) + expert method
Selection of appropriate experts
  > Indicates the number of experts
  > Competence in the field
Additional information confirming the choice of expert method
Establish an expert survey on the criteria or comparison of the importance of the criteria
The arithmetic mean of all experts involved shall be used in the calculation
Degree of importance | Definition
1 | Equal importance
2 | Weak
3 | Moderate importance
4 | Moderate plus
5 | Strong importance
6 | Strong plus
7 | Very strong importance
8 | Very, very strong
9 | Extreme importance
Number of criteria n=3
Number of comparisons= 3(3-1)/2 = 3
5
1/5
Notes: Uz skalas atzīmē vērtību
Pa kreisi faktiskā, pa labi- apgrieztā
All comparisons are positive
Atbilstošu ekspertu izvēle
> Norāda ekspertu skaitu
> Kompetenci attiecīgajā jomā
Papildus informāciju, kas apliecina eksperta metodes izvēli
Izveido ekspertu aptauju par kritērijiem vai kritēriju nozīmīguma salīdzinājumu
Aprēķinā izmanto vidējo aritmētisko vērtējumu no visiem iesaistītajiem ekspertiem

## Slide 19: Multi Criteria Decision Analysis (MCDA) steps
1. Information about alternatives and criteria
Matrix creation
2. Standardization of decision matrix
3. Determination of criteria weight
4. Weighted decision matrix
5. Ideal and anti-ideal option
6. Relative closeness to ideal- solution
7. Priority determination
8. Sensitivity analysis
Literature
analysis
TOPSIS
AHP
Expert method
Define problem
Data collection
Practical task
Notes: Pirmais solis ir apkopot informāciju par alternatīvām un izvēlētajiem kritērijiem
Otrajā aprēķinu solī šie dati tiek normalizēti
Nākamais solis ir datu normalizēšana ar svaru vērtībām un attāluma aprēķins no maksimālajām un minimālajām vērtībām (attālums no ideālā varianta)

## Slide 20: Step 1. Defining decision making problem/ alternatives/ criteria/ data
Input data
 |  |  | Taxi price | 2+(0,64x35km) | 
 |  | Alternatives |  |  | 
 |  | xa1 | xa2 | xa3 | 
 | Criteria | Train | Bus | Taxi | 
i1 | Price, Euro | 1.33 | 2.00 | 24.40 | 
i2 | Time, min | 40 | 50 | 30 | 
i3 | CO2 emissions g/km/pas | 0.07 | 17.30 | 206 | 
i4 | Comfort (evaluation scale 1-10) | 7 | 6 | 10 | 
Data collection
Decision - choose most suitable transport for driving from Riga to Ogre
Information about alternatives
Information about criteria
Riga-Ogre 35km
Expert opinion

## Slide 21: Step 1.1. Creation of TOPSIS matrix (Overview) Given m criteria i, n alternatives a are represented in the decision matrix X = (xai), where i = 1,.., m and a = 1,…, n.
Criteria | Alternatives |  |  |  |  | Normalized (Standardized) decision matrix |  |  |  |  | Weight | Weighted standardized decision matrix |  |  |  |  | Ideal | Anti-Ideal | 
 | xa1 | xa2 | xa3 | … | xan | r1a | r2a | r3a | … | rna | w | va1 | va2 | va3 | … | van | (vA1…vAn) |  | 
i1 |  |  |  |  |  |  |  |  |  |  | w1 |  |  |  |  |  |  |  | 
i2 |  |  |  |  |  |  |  |  |  |  | w2 |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  | w3 |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  | … |  |  |  |  |  |  |  | 
im |  |  |  |  |  |  |  |  |  |  | wn |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | ∑ 1,0 |  |  |  |  |  |  |  | 
AHP
TOPSIS

## Slide 22: Step 2 Standardization of decision matrix
,
where
a alternative, a= 1,...,n
i criteria, i=1,...,m
rai normalized criteria value
 | Alternatives |  |  |  | Standardized decision matrix |  | 
 | xa1 | xa2 | xa3 |  | rai1 | rai2 | rai3
Criteria | Train | Bus | Baltic taxi |  |  |  | 
Price, Euro | 1.33 | 2.00 | 24.40 | 24.52 | 0.05 | 0.08 | 1.00
Time, min | 40.00 | 50.00 | 30.00 | 70.71 | 0.57 | 0.71 | 0.42
CO2 emissions g/km/pas | 0.07 | 17.30 | 206.00 | 206.73 | 0.00 | 0.08 | 1.00
Comfort (evaluation scale 1-10) | 7 | 6 | 10 | 13.60 | 0.51 | 0.44 | 0.74
TOPSIS
Distributive normalization requires that the performances are divided by the square root of the sum of each squared element in a column
=SQRT(xai^2+xa2^2+…xn^2)
Notes: SQRT(xai^2+xa2^2+…xn^2)

## Slide 23
AHP
 | Criteria | More important than | Equally important | Less important than | Criteria | 
Price | i1 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i2 | Time
Price | i1 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i3 | CO2
Price | i1 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i4 | Comfort
Time | i2 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i3 | CO2
Time | i2 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i4 | Comfort
CO2 | i3 | 9 8 7 6 5 4 3 2 | 1 | 2 3 4 5 6 7 8 9 | i4 | Comfort
Actual value
Inverted value
 |  | i1 | i2 | i3 | i4
 | AHP criteria | Price, Euro | Time, min | CO2 emissions g/km/pas | Comfort
i1 | Price, Euro | 1.00 | 5.00 | 8.00 | 5.00
i2 | Time, min | 0.20 | 1.00 | 3.00 | 2.00
i3 | CO2 emissions g/km/pas | 0.13 | 0.33 | 1.00 | 0.25
i4 | Comfort | 0.20 | 0.50 | 4.00 | 1.00
Step 3 Determination of criteria importance

## Slide 24
Price, Euro
Time, min
CO2 emissions g/km/pas
Comfort
Price, Euro | Time, min | CO2 emissions g/km/pas | Comfort
AHP criteria weights
Step 3.1. Creation of AHP comparison matrix
AHP
∑Cij
Matrix of pairwise elements:
Sum the values in each column of the pairwise matrix:
Divide each element in the matrix by its column total to generate a normalized pairwise matrix:
Notes: =1/5
=1/8
=1/3
utt

## Slide 25
AHP
Priority vector (eigen vector) – used as criteria weights in the TOPSIS method
wi1
wi2
wi3
wi4
Step 3.2. AHP matrix normalization, weight determination
Price, Eiro | Time, min | CO2 emissions g/km/pas | Comfort
Price, Eiro
Time, min
CO2 emissions g/km/pas
Comfort
Price, Eiro
Time, min
CO2 emissions g/km/pas
Comfort
AHP criteria weights
Normalization
Divide the sum of the normalized column of matrix by the number of criteria used (n) to generate priority vector:
max = average (consistency vector)
Notes: Normalized criteria value= existing value/ criteria sum value
Eigen vector =average (normalized criteria value) (sum must be 1)

## Slide 26
max = average (consistency vector)
Step 3.3. Verification of consistency of criteria assessments I
AHP
AHP criteria weights
Consistency vector is calculated by multiplying the pairwise matrix by the priority vector:
max is calculated by averaging the value of the Consistency vector:
Consistency vector=MMULT(C4:F4;G12:G15)/G12
max
Cv ij
Notes: CI1 = sum ((i11*ev1)+(i12*ev2)…)/ev1 (tas pats ar mmult) – sareizina vienas kolonnas vērtību ar otras kolonas vērtību un sasummē visus šos reizinājumus, izdala ar attiecīgā kritērija eigenvectoru
Consistency vector =MMULT(C4:F4;G12:G15)/G12
Lambda max = average (consistency vector)
Alonso and Lamata (2006) have computed a regression of the random indices and propose the formulation (see lambda max regression formula)

## Slide 27
AHP
Chart: Criteria weights
| Cena, Eiro | Laiks, min | CO2 izmešu daudzums g/km/pas | Ērtības
 | 0.62338 | 0.17685 | 0.055888 | 0.14388
Step 3.4. Verification of consistency of criteria assessments II
Consistency ratio, CR
RI =VLOOKUP(H10;K11:L26;2)
Criteria weights for further analysis:
Price, Euro
Time, min
CO2 emissions, g/km/pas
Comfort
=IF(H19<0.1;"YES";"NO")
Notes: RI (Random index) =VLOOKUP(H10;K11:L26;2)
{ RI =VLOOKUP(cipars ar ko jāsakrīt (4) ;tabulas sākums:tabulas beigas (abas kolonnas);ņem otro kolonnu)}
Lamda max – eigenvalue
Consistency vector =MMULT(C4:F4;G12:G15)/G12
Lambda max = average (consistency vector)
=IF(H19<0.1;"YES";"NO") var pielikt krāsas – conditional formating, manage rules, format only cells that contains  specific text  iezīmē paraugšūnu [YES]  format  zaļš
ADD --,,-- [NO]  sarkans

## Slide 28: Step 4 Weighted standardized decision matrix
Weights derived from AHP method
,
where
weighted value
wi weight, wi1+wi2+…+wim=1, wi=1,…m
rai normalized criteria value
 |  | Weighted standardized decision matrix |  | 
Criteria | Weight | 1 | 2 | 3
Price, Euro | 0.62 | 0.03 | 0.05 | 0.62
Time, min | 0.18 | 0.10 | 0.13 | 0.08
CO2 emissions g/km/pas | 0.06 | 1.8E-05 | 4.7E-03 | 5.6E-02
Comfort | 0.14 | 0.07 | 0.06 | 0.11
 | 1.00 |  |  | 
 |  | Weighted standardized decision matrix |  | 
Criteria | Weight |  |  | 
Price, Euro | 0.62 | 0.03 | 0.05 | 0.62
Time, min | 0.18 | 0.10 | 0.13 | 0.08
CO2 emissions g/km/pas | 0.06 | 1.8E-05 | 4.7E-03 | 5.6E-02
Comfort | 0.14 | 0.07 | 0.06 | 0.11
 | 1.00 |  |  | 
TOPSIS
A weighted normalized decision matrix is constructed by multiplying the normalized scores by their corresponding weights wi :

## Slide 29: Step 5 Ideal and anti-ideal option
Weighted results are taken into account to compare the ideal and anti-ideal virtual action.
Each weighted indicator is compared with the maximum and minimum values corresponding to the respective criterion. The sum of the squares of the criteria difference for each alternative from the maximum value is used to determine the total distance of the alternative to the ideal solution.
where
distance for each action to the ideal solution
distance for each action to the anti-ideal solution
TOPSIS
N-dimensional Euclidean distance (L2) is used here, but also another metric could be adopted (e.g. L1, the Manhattan metric)

## Slide 30
=MAX(va1:va3)
and where
distance for each action to the ideal solution
distance for each action to the anti-ideal solution
=MIN(va1:va3)
Criteria | Standardized decision matrix |  |  | Ideal solution | Anti-ideal solution | Distance for each action to the ideal solution |  |  | Distance for each action to the anti-ideal solution |  | 
 | va1 | va2 | va3 |  |  |  |  |  |  |  | 
Price, Euro | 0.03 | 0.05 | 0.62 | 0.03 | 0.62 | 0.0000 | 0.0003 | 0.3441 | 0.3441 | 0.3244 | 0.0000
Time, min | 0.10 | 0.13 | 0.08 | 0.08 | 0.13 | 0.0006 | 0.0025 | 0.0000 | 0.0006 | 0.0000 | 0.0025
CO2 emissions g/km/pas | 1.8E-05 | 4.7E-03 | 5.6E-02 | 0.00 | 0.06 | 0.0000 | 0.0000 | 0.0031 | 0.0031 | 0.0026 | 0.0000
Comfort | 0.07 | 0.06 | 0.11 | 0.11 | 0.06 | 0.0010 | 0.0018 | 0.0000 | 0.0001 | 0.0000 | 0.0018
 |  |  |  |  |  | 0.04 | 0.07 | 0.59 | 0.59 | 0.57 | 0.07
TOPSIS
Notes: SQRT(SUM(V5:V8))

## Slide 31: Step 6 Calculate relative closeness
Calculate the relative closeness coefficient of each alternative:
where
Ca relative closeness to the ideal solution
0 ≤ Ca ≤ 1, i = 1,2,…,m.
The closeness coefficient is always between 0 and 1, where 1 is preferred action.
 |  |  | Vilciens | Autobuss | Baltic taxi
(MAX) |  |  | 0.04 | 0.07 | 0.59
(MIN) |  |  | 0.59 | 0.57 | 0.07
(MAX) + (MIN) |  |  | 0.63 | 0.64 | 0.65
(MIN)/((MAX) +(MIN)) |  |  | 0.94 | 0.89 | 0.10
 |  |  | Vilciens | Autobuss | Baltic taxi
 |  |  | 0.04 | 0.07 | 0.59
 |  |  | 0.59 | 0.57 | 0.07
 |  |  | 0.63 | 0.64 | 0.65
 |  |  | 0.94 | 0.89 | 0.10
TOPSIS
Chart: MCDA TOPSIS result
| Train | Bus | Taxi
 | 0.93589 | 0.89392 | 0.10007

## Slide 32: Step 7 Sensitivity analysis
W’k1 = ßk*w’,k=1,2,3…n
wk1 – weight being imposed a disturbance
ßk – this variable is defined as the unitary variation ratio of wk after disturbance
TOPSIS
In order to check the influence of attribute distributions on the results of the TOPSIS method, the significances of equal size attributes are chosen
Initial weights are considered as w’=1/n (where n = number of parameters selected for assessment)
Unitary variation ratio ßk | Values less than 1 |  | ßk' | Values larger than 1 |  | 
 | ßk1 | ßk2 | 1 | ßk3 | ßk4 | ßk5
wk1 | W’k11 = ßk1*w’ | W’k12 = ßk2*w’ | w’=1/n | W’k13 = ßk3*w’ | W’k14 = ßk3*w’ | W’k15 = ßk3*w’
wk2 | W’k21 = (1-w’k11)/(n-1) | W’k22 = (1-w’k12)/(n-1) | w’=1/n | W’k23 = (1-w’k13)/(n-1) | … | …
wk3 | W’k21 = (1-w’k11)/(n-1) | W’k23 = (1-w’k12)/(n-1) | w’=1/n | … | … | …
wk4 | W’k21 = (1-w’k11)/(n-1) | W’k24 = (1-w’k12)/(n-1) | w’=1/n | … | … | …
Unitary variation ratio ßk | 0.01 | 0.5 | 1 (n=4) | 1.5 | 2 | 3
Price, Eiro | 0.0025 | 0.125 | 0.25 | 0.38 | 0.50 | 0.75
Time, min | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08
CO2 g/km/pas | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08
Comfort | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08
∑ | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
Other weights distribution are changed based on weight imposed to disturbance
w’=1/n (n = number of factors)

## Slide 33: Step 7.1. Sensitivity analysis - obtaining relative closeness to the ideal solution with newly acquired weights
TOPSIS
Unitary variation ratio ßk | 0.01 | 0.5 | 1 | 1.5 | 2 | 3 |  |  |  |  |  |  | 
Price, Eiro | 0.0025 | 0.125 | 0.25 | 0.38 | 0.50 | 0.75 |  | 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Time, min | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Train | 0.79 | 0.81 | 0.84 | 0.88 | 0.92 | 0.97
CO2 g/km/pas | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Bus | 0.69 | 0.70 | 0.76 | 0.82 | 0.87 | 0.94
Comfort | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Taxi | 0.29 | 0.28 | 0.23 | 0.17 | 0.12 | 0.05
 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  |  |  | 
Unitary variation ratio ßk | 0.01 | 0.5 | 1 | 1.5 | 2 | 3 |  |  |  |  |  |  | 
Price, Eiro | 0.0025 | 0.125 | 0.25 | 0.38 | 0.50 | 0.75 |  | 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Time, min | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Train | 0.79 | 0.81 | 0.84 | 0.88 | 0.92 | 0.97
CO2 g/km/pas | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Bus | 0.69 | 0.70 | 0.76 | 0.82 | 0.87 | 0.94
Comfort | 0.33 | 0.29 | 0.25 | 0.21 | 0.17 | 0.08 | Taxi | 0.29 | 0.28 | 0.23 | 0.17 | 0.12 | 0.05
 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 |  |  |  |  |  |  | 
Replace initial attribute weights with newly acquired weights in TOPSIS matrix
(relative closeness to the ideal solution) with newly acquired weights:
Make sure that sensitivity analysis are done for all criteria
It is possible to use other sensitivity analysis methods:
(Different mathematical calculation approach)
Alinezhad, Alireza. (2011). Sensitivity Analysis of TOPSIS Technique: the Result of Change in the Weight of one attribute on the Final Ranking of Alternatives”. Journal of optimization in Industrial Engineering (OIE),Vol. 7, No. 1, pp. 23-28, 2011..
Peiyue Li, Hui Qian, Jianhua Wu & Jie
Chen (2013) Sensitivity analysis of TOPSIS method in water quality assessment: I. Sensitivity to the parameter weights DOI: 10.1007/s10661-012-2723-9
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.86153 | 0.85725 | 0.84039 | 0.80559 | 0.75024 | 0.59166
Bus | 0.80799 | 0.7965 | 0.75577 | 0.68479 | 0.58869 | 0.33497
Taxi | 0.1767 | 0.1884 | 0.22944 | 0.30024 | 0.3959 | 0.65157

## Slide 34
Sensitivity analysis (SA) results
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.86153 | 0.85725 | 0.84039 | 0.80559 | 0.75024 | 0.59166
Bus | 0.80799 | 0.7965 | 0.75577 | 0.68479 | 0.58869 | 0.33497
Taxi | 0.1767 | 0.1884 | 0.22944 | 0.30024 | 0.3959 | 0.65157
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.7846 | 0.79961 | 0.84039 | 0.88575 | 0.92292 | 0.97176
Bus | 0.6908 | 0.70769 | 0.75577 | 0.81188 | 0.85759 | 0.9063
Taxi | 0.30247 | 0.2831 | 0.22944 | 0.1677 | 0.11522 | 0.043302
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.90689 | 0.89012 | 0.84039 | 0.76656 | 0.6734 | 0.43437
Bus | 0.81347 | 0.80051 | 0.75577 | 0.68043 | 0.58119 | 0.32656
Taxi | 0.1711 | 0.18432 | 0.22944 | 0.30458 | 0.40338 | 0.66015
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2
Train | 0.79384 | 0.8057 | 0.84039 | 0.88269 | 0.91962
Bus | 0.68671 | 0.70449 | 0.75577 | 0.81769 | 0.8719
Taxi | 0.29057 | 0.27519 | 0.22944 | 0.17195 | 0.11996

## Slide 35: Comparison of results of three SA methods
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5
Train | 0.60537 | 0.80978 | 0.93589 | 0.99214
Bus | 0.43737 | 0.71345 | 0.89392 | 0.96832
Taxi | 0.54042 | 0.27836 | 0.10007 | 0.012675
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.9489 | 0.94594 | 0.93589 | 0.91815 | 0.89279 | 0.8169
Bus | 0.92576 | 0.91795 | 0.89392 | 0.85656 | 0.80852 | 0.68161
Taxi | 0.067007 | 0.075277 | 0.10007 | 0.13773 | 0.18558 | 0.31145
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2
Train | 0.79384 | 0.8057 | 0.84039 | 0.88269 | 0.91962
Bus | 0.68671 | 0.70449 | 0.75577 | 0.81769 | 0.8719
Taxi | 0.29057 | 0.27519 | 0.22944 | 0.17195 | 0.11996
Chart: Unitary variation ratio
| 0.01 | 0.5 | 1 | 1.5 | 2 | 3
Train | 0.86153 | 0.85725 | 0.84039 | 0.80559 | 0.75024 | 0.59166
Bus | 0.80799 | 0.7965 | 0.75577 | 0.68479 | 0.58869 | 0.33497
Taxi | 0.1767 | 0.1884 | 0.22944 | 0.30024 | 0.3959 | 0.65157
Chart: Weight distribution
| 0.1 | 0.25 | 0.5 | 0.75
Train | 0.91527 | 0.8658 | 0.72173 | 0.51846
Bus | 0.85085 | 0.76123 | 0.53862 | 0.16234
Taxi | 0.14344 | 0.2325 | 0.45378 | 0.83354
W’=1/n (full calculations see in slides before)
W’2=w2+∆2
W’2 = W2*Wk
j=1,3,4

## Slide 36: References
….
….

## Slide 37: Bioeconomy general assessment methods and tools

## Slide 38: Specifc aim and objectives
The unit will aim to provide an overview of bioeconomy evaluation methods
  Explain the need for bioeconomy evaluation
  Recognize the issues regarding bioeconomy evaluation
  Identify bio-based product values

## Slide 39: Keywords
Bioeconomy
Economic indicators
Evaluation
Development
Data

## Slide 40: Contents
Economic activity
Keeping treack of economic activity
Evaluation of bioeconomy
Evaluation of the bioeconomy potential (Nexus and Cascade Approaches)

## Slide 41: What is the economy?
It is the whole production and consumption of goods. Usually in specific
Notes: Let’s start with the basic definition of economy. It is the whole production and consumption of goods and services in specific area. That area might be a country, country, geographical region or specifically established areas. For example Europe Economic Area. Usualy specific rules are set within these areas like taxes and tarifs and so on.

## Slide 42: OECD Main Economic Indicators (MEI)
Balance of payments
Business tendency and consumer opinion surveys
Composite leading indicators
Financial statistics
Industry
International trade
Labour market statistics
Consumer price indices
Producer price indices
Purchasing power parities (PPP)
Comparative price level
Quarterly national accounts

## Slide 43: How to evaluate bioeconomy?
Industries have differing resolutions. One is tracking its raw material with great precision, other has more rough approach.

## Slide 44: EU Bioeconomy Monitoring System dashboards
https://knowledge4policy.ec.europa.eu/visualisation/eu-bioeconomy-monitoring-system-dashboards_en
Notes: On the slide you can see how the depicted information is giving insight into sustainability aspect of bioeconomy. Data on social, economic and environmental impact is shown. Nevartheless, indicators are usefull because they allow to track progress. Hence, chosen criteria can be tracked annually and policies can be adjusted acordingly.

## Slide 45: Low input farms

## Slide 46: Low vs. High input farms
LOW
HIGH

## Slide 47: Biomass stock
https://forest-energy-atlas.luke.fi/
Firewood in LT
Logging residues in LV

## Slide 48: Green economy
Bioeconomy – trade of bio-based goods and services
Circular economy - The circular economy is a model of production and consumption, which involves sharing, leasing, reusing, repairing, refurbishing and recycling existing materials and products as long as possible. In this way, the life cycle of products is extended and waste is reduced to a minimum.

## Slide 49: Circular bioeconomy
Although biogas as an energy source falls into the fifth category, its production principle and by-products are very different from the production of other fuels. The production of biogas in special biogas reactors produces both the biogas itself and the digestate, which is a nutrient-rich substrate and can be used for soil improvement
Stegmann et al. 2020 The circular bioeconomy: Its elements and role in European bioeconomy clusters

## Slide 50: Soil improvements
Adding organic matter and biochar to soil helps to retain moisture and store carbon that otherwise could be released in the atmosphere in the form of CO2
In addition to organic matter, digestate has many macro and micro nutrients.
ORGANIC FERTILIZER
ORGANIC MATTER
SOIL NUTRIENTS
MICROORGANISMS
PLANT NUTRIENTS

## Slide 51: Bio-based value

## Slide 52: Biomass uses
In the EU Bioeconomy Monitoring System dashboards only three categories have been represented:
Materials
Energy
Food and feed
https://knowledge4policy.ec.europa.eu/visualisation/eu-bioeconomy-monitoring-system-dashboards_en

## Slide 53: Waste and bioresource streams
53

## Slide 55: Boundaries

## Slide 56: Maze to kernel
product
By-product/waste

## Slide 57: Stover to product
product
By-product/waste
Corn stover can replace lumber for some applications.

## Slide 58: Maze to kernel
product
By-product/waste
Corn cob residues can be used for thermal insulation.

## Slide 59: Maze to starch production
Notes: Pārtika vs 1.paaudzes biodegviela
Kukurūzas graudi pārtikā, pārējais 2. paaudzes biodegvielā
Kukurūzas graudi pārtikā, pārējais 2. paaudzes biodegvielā, vālīšu serdes izolācija (Corn's cob as a potential ecological thermal insulation material) vai ksilāns

## Slide 60: Xylan
CORN COB
Alkalyne extraction
Ultrasonification
(40% xylan yield)
Anti-inflamatory
antimicrobial

## Slide 61: By-product utilization index
Xylan, fatty acids
Kernels, feed
Stover boards, packing peanuts
Biogas
Solid fuel

## Slide 62: Cascading value
Cascade use and the management of product lifecycles

## Slide 63
Investments (CAPEX) | Investment sum | Sum of plant investments including auxiliary plants, additional costs (e.g. financing, land fees), plus extension or optimisation
Investment costs (OPEX) | Write-offs | Under consideration of the respective technical service life
 | Imputed interest | Capital return
 | Maintenance | Costs for service and maintenance, as well as a maintenance reserve for the biorefineries
 | Taxes | Property taxes related to the investment
 | Insurance | Biorefinery plant insurance costs
 | Administration | Administration costs associated with the investment

## Slide 64
Material and energy stream costs | Material | Expenses from material purchases
 | Electricity | Expenses from energy consumed
 | Heat | Calculated based on the supplied quantity of heat and the sale price
 | Labour | Labour costs for operations, maintenance and management
 | Other | Other costs not recorded elsewhere
 | Overheads | Additional costs for overhead
Overall evaluation | Operating results | Revenues minus costs (if necessary under consideration of other calculated costs)
 | Net present value | Sum of all discounted net payments (income minus expenses) attributable to the investment at this time

## Slide 65: Economic assessment of the project
𝑂 = 𝐸𝑡 − (∑ 𝐼𝑛 + ∑ 𝐶𝑛 )
𝑶 = operating results
𝑬𝒕 = sum of revenues in the period t
𝑰𝒏 = sum of investment related costs in the period t
𝑪𝒏 = sum of operation related costs in the period t
𝐶0 = −𝐼 + 𝐸𝑡 ∗ 𝐴𝑡 ∗ (1 + 𝑖) −𝑇 + 𝑇 ∗ 𝐴𝑡 ∗ (1 + 𝑖) 𝑇
𝐶0 = net present value
𝐴𝑡 = sum of payments in the period t
𝑖 = discount rate

## Slide 66: List of References
[1] “Circular economy: definition, importance and benefits | News | European Parliament.” [Online]. Available: https://www.europarl.europa.eu/news/en/headlines/economy/20151201STO05603/circular-economy-definition-importance-and-benefits. [Accessed: 13-Dec-2021].
[2] P. Stegmann, M. Londo, and M. Junginger, “The circular bioeconomy: Its elements and role in European bioeconomy clusters,” Resour. Conserv. Recycl. X, vol. 6, no. December 2019, p. 100029, 2020, doi: 10.1016/j.rcrx.2019.100029.
[3] E. G. Pellets, “Comparative Energy Properties of Torrefied Pellets in Relation to Pine and Elephant Grass Pellets,” vol. 13, no. 2, pp. 2898–2906, 2018.
[4] JRC, BBI JU, and IEA Bioenergy, “Joint survey on bioeconomy policy developments in different countries,” p. 34, 2018.
[5] eurostat, “Manual on waste statistics A handbook for data collection on waste generation and treatment.” p. 143, 2013, doi: 10.2785/4198.
[6] M. Khanna and N. Paulson, “To Harvest Stover or Not: Is it Worth it?,” Farmdoc Dly., vol. 6, no. 32, pp. 1–5, 2016.
[7] “Corn instead of wood? $15 million CornBoard plant coming to Iowa | Woodworking Network.” [Online]. Available: https://www.woodworkingnetwork.com/news/woodworking-industry-news/corn-instead-wood-15-million-plant-coming-iowa. [Accessed: 14-Dec-2021].
[8] R. Zhang et al., “Comprehensive utilization of corn starch processing by-products: A review,” Grain Oil Sci. Technol., vol. 4, no. 3, pp. 89–107, Sep. 2021, doi: 10.1016/J.GAOST.2021.08.003.
[9] I. Vamza, A. Kubule, L. Zihare, K. Valters, and D. Blumberga, “Bioresource utilization index – A way to quantify and compare resource efficiency in production,” J. Clean. Prod., p. 128791, Aug. 2021, doi: 10.1016/J.JCLEPRO.2021.128791.
[10] M. Kalverkamp, A. Pehlken, and T. Wuest, “Cascade use and the management of product lifecycles,” Sustain., vol. 9, no. 9, 2017, doi: 10.3390/su9091540.
[11] S. Chovau, D. Degrauwe, and B. Van Der Bruggen, “Critical analysis of techno-economic estimates for the production cost of lignocellulosic bio-ethanol,” Renew. Sustain. Energy Rev., vol. 26, pp. 307–321, 2013, doi: 10.1016/j.rser.2013.05.064.

## Slide 67: Synopsis
This lecture gives an insight into:
The Multi Criteria Decision Analysis (MCDA) and specific practical applications
The explanation of the need for bioeconomy evaluation
Recognization of the issues regarding bioeconomy evaluation
Identification of bio-based product values
Presentation of the Cascade and Nexus approaches
Notes: Summary of contents and learners achievments

## Slide 68: Short-bio
M.sc.ing. Antra Kalnbaļķīte
Scopus Author ID: 57194541789
H-index = 2
Reasercher and lecturer in Institute of Energy Systems and Environment at Riga Technical University
Main research area: sustainable education, bioeconomy

## Slide 69: Short-bio
M.sc.ing. Ilze Vamža
Researcher Ilze Vamža is an environmental scientist with biology background.
Assistant at the Riga Technical University’s course Environmental technologies 2
Lecturer on Biotechnology course
69